Preamp Carrier Board Periodic Noise Issue and Solution
IDLAB	3/27/2013
Objective
We saw ~40kHz periodic noise at the output of the preamps. They are typically around 80 mV peak-to-peak, which could affect the MPPC signals. It becomes an problem for data taking, we have to solve it.

Pic-FujiHallKEK: This photo was taken at Fuji Hall, KEK.
~38kHz

The upper blue signal was the MPPC signal from the Sci-Fi Tracker.
The lower green signal was from a carrier board with ceramic	capcitors on R1 and R2.

Test Setup
Pic-Setup1
Pic-Setup2

Pic-Setup3: Where and how I soldered the Tantalum capacitors.

+
+
+

Notes
  - For all the plots below, the green line is the input signal from preamp.
  - When testing, the scope probe is attached to the test point on TARGET4 daughter card.
  - The purple region is the FFT of the input signal(green line).
  - More details about testing and the saved waveform files can be found here:
    https://drive.google.com/folderview?id=0BxDOJC6YgEhiTUZhaThjcDhZdkE&usp=sharing
  - Table of scales for the FFT measurements.
Scope H. Scale	Vertical Scale	Offset	Horizontal Scale	Position
20 us	20 dB/div	-45dBm	200 MHz/div	1.0 GHz
50 us	20 dB/div	-45dBm	100 MHz/div	500 MHz
100 us	20 dB/div	-45dBm	50 MHz/div	250 MHz

Background Noise

Pic-bg032701: The scope probe is not attached and the lights in the room are	on.

~40 kHz

~40kHz

As we zoom in, the 40 kHz periodic noise becomes clear. The closer look is shown in Pic-bg032702.
Pic-bg032702: A zoom-in look of Pic-bg032701. It's clear that the 40kHz	periodic noise exists in the background.

~40kHz

The 40kHz noise is from the Fluorescent lamps. As I turned off the lights, the 40kHz periodic noise disappeared. You can find more information at:

1. Interference Problems of Fluorescent Lamps Operating on High Frequency Electronic	Ballasts with Infrared Remote Control Equipment and Infrared Simultaneous	Interpretation System
http://www.emsd.gov.hk/emsd/e_download/pee/infrared_interference_emsdweb.pdf
    1. Silence of the Lamps: Reducing radio frequency interference from small fluorescent lamps
      http://www.randombio.com/fluorescent-lamp-interference.html

Causes of the Issue
The voltage regulator LM337 on preamp carrier board needs input and output by-pass Tantalum capacitors for stability. Without them, the 40kHz background noise picked up by the long ribbon cable will be amplified through the preamps.

Without an input by-pass Tantalum capacitor, the periodic noise always appears even with an output by-pass Tantalum capacitor.
Pic-PAC14.03: CX1 was replaced with a 2.2 uF Tantalum capacitors and CX2 was	removed on carrier board#14.

~50kHz
      FFT Scale: vertical=20dB/div; offset=-45dBm
horizontal=100MHz/div; position(center line)=500MHz

Adding a input by-pass Tantalum capacitor, the periodic noise always disappears.

It has been tested on 4 different preamp carrier boards with 2.2 uF, 4.7 uF and 1uF Tantalum capacitors. They worked equally well.

Pic-PAC12.14: No capacitor on CX1(output) and 2.2 uF Tantalum Capacitor on	CX2(input). 2 preamps on the carrier board#12.
      FFT Scale: vertical=20dB/div; offset=-45dBm
1. horizontal=100MHz/div; position(center line)=500MHz
  Pic-PAC14.05: Both CX1(output) and CX2(input) were replaced with 2.2 uF
    ~100MHz

            Tantalum capacitors.
        1. FFT Scale: vertical=20dB/div; offset=-45dBm
  horizontal=100MHz/div; position(center line)=500MHz

Pic-PAC12.16: No capacitor on CX1 and 2.2 uF Tantalum Capacitor on CX2.
15 preamps on the carrier.
      FFT Scale: vertical=20dB/div; offset=-45dBm
1. horizontal=100MHz/div; position(center line)=500MHz

Pic-PAC3.21: 4.7 uF Tantalum capacitors on CX1(output) and CX2(input).
15 preamps on the carrier.
FFT Scale: vertical=20dB/div; offset=-45dBm
horizontal=100MHz/div; position(center line)=500MHz

Pic-PAC11.25: 2.2uF Tantalum capacitors on both CX1(output) and CX2(input).
15 preamps on the carrier.
FFT Scale: vertical=20dB/div; offset=-45dBm
horizontal=100MHz/div; position(center line)=500MHz

Conclusion
After testing on preamp carrier #14, #12, #3 and #11, it becomes very clear that in order to solve the noise issue, we MUST solder an input by-pass Tantalum capacitor.
We need an output Tantalum capacitor as well.
The ceramic capacitors doesn't work well. They reduce the periodic noise, but the results are not stable.

Procedure:
1. Desolder CX1 and CX2 on the preamp carrier board.
2. Follow the diagram Pic-Setup3.
  The '+' side(The side closer to “bar”) of the Tantalum capacitor should be connected to 'GND' for both CX1 and CX2.