## Slide 1: strip detector with surrounding guardring Dimension Details
6750um (active edge boundaries)
6500um active width (130strips x 50um)
Entrance window for x-rays
2415um

## Slide 2: Pad layout for strip detector w/surrounding Guard Ring
Backside contact: opening 196um x 46um, both left and right bottom corner
Pad opening: 32umx192um
Guard ring
Pad opening
32umx192um

## Slide 3: Cross section of GR device Active device on support substrate
2415um
Active device
Support substrate
75um
(plasma diced)
300um
(wafer-saw)
2415um
50um-100um?

## Slide 4: Strip Detector w/Surrounding guard ring: entrance window
Guard ring: 5um wide
From guard ring to entrance window: 20um
“Dead” region = guard ring width + distance from guard ring to edge + ½ distance from guard ring to pixel =33um
From guard ring to pixel: 15um
Dead region boundary

## Slide 5: Old Baseline strip detector: 3-sides guard ring
6750um (active edge boundaries)
6500um active width (130strips x 50um)
-2 outer strips tied to guard-ring
2445um
Entrance window for x-rays

## Slide 6: Cross section of old baseline device Active device on support substrate
2445um
Active device
Support substrate
75um
(plasma diced)
300um
(wafer-saw)
2445um
50um-100um?

## Slide 7: Old Baseline strip detector
Backside contact: opening 196um x 46um, both left and right bottom corner
Pad opening: 32umx192um
Strip pitch: 50um
130 pixels, active width = 6500um
Guard ring contact

## Slide 8: Old Baseline w/extra distance
Backside contact: opening 196um x 46um, both left and right bottom corner
Guard ring contact
Extra 350um
Total height 2775um
Topcell: top_extra_pad_distance

## Slide 9: Old Baseline entrance window (with or without extra pad distance)
From pixel diffusion to entrance window: 50um
Pixel diffusion starts 50um from entrance window, but “dead” region would be limited to sidewall p-diffusion on entrance window, ~1um